## Slide 1
Hello Everyone!
So, I had this opportunity to create this tool which is a Web Application for Calculating Emission Factors. Before going to this tool
first I would like to define the Emission Factors for those who are not familiar with this term.
Emission Factors (EFs) are coefficients that quantify the amount of greenhouse gas (GHG) emissions released per unit of activity or energy consumed. They are expressed in units such as kg CO₂e per kWh (for electricity) or kg CO₂e per liter (for fuel combustion). Emission factors help convert energy consumption, industrial activities, or transportation data into their corresponding carbon dioxide equivalent (CO₂e) emissions to estimate environmental impact.

## Slide 2: Project Overview
I created this web application designed to help users calculate Scope 1 and Scope 2 emission factors based on fuel type, eGRID subregions, and selected output units.

## Slide 3
Global Warming Potential (GWP) is a critical factor in greenhouse gas (GHG) emissions calculations because different gases have varying abilities to trap heat in the atmosphere. Since emissions data is often reported in CO₂ equivalent (CO₂e), selecting the correct GWP value ensures that non-CO₂ greenhouse gases (like methane and nitrous oxide) are properly converted to their CO₂-equivalent impact.
AR5 (Fifth Assessment Report) and AR4 (Sixth Assessment Report) are major climate science reports published by the Intergovernmental Panel on Climate Change (IPCC). These reports provide the latest scientific understanding of climate change, global warming potential (GWP), greenhouse gas (GHG) emissions, and climate projections.
GWP measures how much heat a gas traps in the atmosphere over a specific time period, relative to CO₂.
Carbon Dioxide (CO₂) → GWP = 1 (Baseline gas).
Methane (CH₄) → GWP = 27-30 (depending on the GWP timeframe used).
Nitrous Oxide (N₂O) → GWP = ~273 (over 100 years, per IPCC AR6).
We categorized the emissions in Scope 1, scope2 and scope 3 categories for any Industries.
Scope 1 is (Direct Emissions from Fuel Combustion & Industrial Processes)
Scope 2 is (Indirect Emissions from Purchased Electricity)
Scope 3 is (Indirect Emissions from Supply Chain & Business Activities)

## Slide 4: Key Features
- Interactive UI with dropdowns for user inputs
- Automated Conversion of emission values into different units
- Info icon is provided for user guidance
- Its easy access is another key feature

## Slide 5: Tech Stack & Tools Used
- **Python**: Backend scripting and data processing

## Slide 6: Deployment Process
1. Developed and tested the app locally using Streamlit.
2. Pushed the project to GitHub for version control.
3. Hosted the app on **Streamlit Community Cloud** for easy access.
Streamlit.io is an open-source Python framework for building interactive web applications with minimal coding effort. It is especially popular among data scientists, engineers, and analysts for quickly converting Python scripts into user-friendly web apps.
4. Users can now access the tool via a web browser without needing to install anything.

## Slide 7: Conclusion
The Emission Factor Tool will be used internally, it could be useful for calculating emission factors As it simplifies emissions calculations.